## Slide 1: Lecture 17: 3D Printing and Inventor

## Slide 2: Download Inventer
www.Studentsupport.Newhaven.edu/first-year-engineering-students

## Slide 3
How do you design something?
Why you might 3D print?
What can you print
3D Printing 101
Getting ready to 3D Print
Software for 3D modeling

## Slide 4: Engineering Problem Solving Approach
Gather Data & Verify Accuracy
Problem Identification
Analysis/Design
Application
Comprehension
SOLUTION
evaluate your analysis or
Design
do a solution check, then decide if you need to loop back or not.
Rapid Prototyping
Notes: Application – Here you evaluate your analysis
Comprehension – Here you do a solution check, then decide if you need to loop back or not.

## Slide 5: Classic Development Cycle
Concept definition
Requirements definition
Preliminary design
Detailed design
Implementation
Testing/acceptance
[Griping]
Copyright © 2016, Beforeworks [1]. This material is copyrighted and not to be used outside of this course.
Notes: If a product or idea doesn’t meet all of the requirements, it shouldn’t be considered as a potential solution in the current state.
Ideas should be able to be judged along a “Sliding scale” for each criteria, in which you can clearly identify okay, good, better, best for each criteria with relation to possible solutions. As an example, low cost vs less than $$.
Quiz question1- select the one that isn’t a requirement.
Quiz question2- select the one that isn’t a criteria.

## Slide 6: Rapid Prototyping Cycle [2]
Concept Design
Implement skeletal system
User evaluation and concept refinement
Implementation of refined requirements
User evaluations and concept refinement
Implementation of refined requirements
Repeat
“Early development of a small-scale prototype used to test out certain key features of the design.”
Notes: If a product or idea doesn’t meet all of the requirements, it shouldn’t be considered as a potential solution in the current state.
Ideas should be able to be judged along a “Sliding scale” for each criteria, in which you can clearly identify okay, good, better, best for each criteria with relation to possible solutions. As an example, low cost vs less than $$.
Quiz question1- select the one that isn’t a requirement.
Quiz question2- select the one that isn’t a criteria.

## Slide 7: Rapid Prototyping
Prototype for a purpose: develop a question your prototype should answer.
Build an aquaponics system
How much oxygen does pump X put into water?
What material can I use for grow-towers that will be mold-resistant?
Develop a sensor system
How accurate is the sensor when detecting Y?
How much data is collected in continuous-monitoring system?

## Slide 8: Why might you 3D print?
Speed- complex designs printed within a few hours.
https://www.3dhubs.com/knowledge-base/advantages-3d-printing

## Slide 9: Why might you 3D print?
Speed- complex designs printed within a few hours.
Single-step building (in some machines)
https://www.3dhubs.com/knowledge-base/advantages-3d-printing
Notes: One of the biggest concerns for a designer is how to manufacture a part as efficiently as possible. Most parts require a large number of manufacturing steps to be produce by traditional technologies. The order these steps occur affects the quality and manufacturability of the design.
Consider a custom steel bracket that is made via traditional manufacturing methods:
Similarly to additive manufacturing, the process begins with a CAD model. Once the design is finalized, fabrication begins with first cutting the steel profiles to size. The profiles are then clamped into position and welded one at a time to form the bracket. Sometimes a custom jig will need to be made up to ensure all components are correctly aligned. The welds are then polished to give a good surface finish. Next holes are drilled so the bracket can be mounted on the wall. Finally, the bracket is sandblasted, primed and painted to improve its appearance.

## Slide 10: Why might you 3D print?
Speed- complex designs printed within a few hours.
Single-step building (in some machines)
Cost: save on machine cost, machine operating cost, and labor
https://www.3dhubs.com/knowledge-base/advantages-3d-printing
Notes: The cost of manufacture can be broken down into 3 categories; machine operation costs, material cost and labor costs.
Machine operation costs: Most desktop 3D printers use the same amount of power as a laptop computer. Industrial additive manufacturing technologies consume a high amount of energy to produce a single part. However, the ability to produce complex geometries in a single step results in higher efficiency and turnaround. Machine operation costs are typically the lowest contributor to the overall cost of manufacture.
Material costs: The material cost for additive manufacturing varies significantly by technology. Desktop FDM printers use filament coils that cost around $25 per kg, while SLA printing requires resin that retails around $150 per liter. The range of materials available for additive manufacturing makes quantifying a comparison with traditional manufacturing difficult. Nylon powder used in SLS costs around $70 per kg, while comparable nylon pellets used in injection molding can be purchased for as little as $2 - $5 per kg. Material costs are the biggest contributor to the cost of a part made via additive manufacturing.
Labor costs: One of the main advantages of 3D printing is the the low cost of labor. Post-processing aside, the majority of 3D printers only require an operator to press a button. The machine then follows a completely automated process to produce the part. Compared to traditional manufacturing, where highly skilled machinists and operators are typically required, the labor costs for a 3D printer are almost zero.
Additive manufacturing at low volumes is very competitively costed compared to traditional manufacturing. For the production of prototypes that verify form and fit, it is significantly cheaper than other alternative manufacturing methods (e.g. injection molding) and is often competitive for manufacturing one-off functional parts. Traditional manufacturing techniques become more cost-effective as volume increases and the high setup costs are justified by the large volumes of production.

## Slide 11: Why might you 3D print?
Speed- complex designs printed within a few hours.
Single-step building (in some machines)
Cost: save on machine cost, machine operating cost, and labor
Risk mitigation
https://www.3dhubs.com/knowledge-base/advantages-3d-printing
Notes: Ordering a faulty prototype costs the designer time and money. Even small changes in a mold or fabrication method may have a large financial impact.
Being able to verify a design by printing a production-ready prototype before investing in expensive manufacturing equipment (e.g. molds or tooling and jigs) eliminates the risk during the prototyping process. This helps with building confidence in one's design before making the large investments required for the mass production level.

## Slide 12: Why might you 3D print
And MORE
  Complexity and design freedom
  Customization
  Sustainability
https://www.3dhubs.com/knowledge-base/advantages-3d-printing
Notes: Do not have to be bound by constraints of traditional manufacturing, i.e., angles, undercuts, tool access.
Easily customize for one-off productions. Especially suitable when sizes quickly change or personalizations.
Depending on traditional manufacturing methods, there can be a lot of waste. Additive manufacturing = less waste as only using what is needed to build onto design.

## Slide 13: What can you print?
https://www.google.com/url?sa=i&rct=j&q=&esrc=s&source=images&cd=&cad=rja&uact=8&ved=2ahUKEwju6LHpx8rdAhUFMXwKHW6OCXQQjRx6BAgBEAU&url=http%3A%2F%2Fwww.3dprintertx.com%2F3d-printing-rapid-prototyping%2F&psig=AOvVaw0JIRxc4lroRel4r5_Uv8rL&ust=1537566500460835
https://www.google.com/url?sa=i&rct=j&q=&esrc=s&source=images&cd=&cad=rja&uact=8&ved=2ahUKEwiUtc6kx8rdAhUywMQHHT6_CeoQjRx6BAgBEAU&url=https%3A%2F%2Fwww.digitaltrends.com%2Fcool-tech%2Fuseful-3d-printed-household-items%2F&psig=AOvVaw2ky_oi23QGNjNUcogzqaSn&ust=1537566260577584
https://static.makeuseof.com/wp-content/uploads/2016/08/3d-printing-useful-at-home-toothpaste-tube-squeezer.png
Notes: Useful Gadgets/tools
Fun
Prototypes of larger items that will ultimately be manufactured

## Slide 14: 3D Printing 101- Overview
3D printing is considered additive manufacturing: layers of materials are built up to create a solid object.
General steps:
CAD Model- digital rendering
Convert to STL file + internal file manipulation
Printing- calibration, maintenance, and materials selection
Removal and Post-processing- base removal, sanding,
Notes: A critical stage in the additive manufacturing process that varies from traditional manufacturing methodology is the requirement to convert a CAD model into an STL (stereolithography) file. STL uses triangles (polygons) to describe the surfaces of an object. A guide on how to convert a CAD model to an STL file can be found here. There are several model limitations that should be considered before converting a model to an STL file including physical size, watertightness and polygon count.
Once a STL file has been generated the file is imported into a slicer program. This program takes the STL file and converts it into G-code. G-code is a numerical control (NC) programming language. It is used in computer-aided manufacturing (CAM) to control automated machine tools (including CNC machines and 3D printers). The slicer program also allows the designer to customise the build parameters including support, layer height, and part orientation.

## Slide 15: 3D Printing 101- Types of printing

## Slide 16: 3D Printing 101- Popular types of printing
Material Extrusion: material is squeezed out of the nozzle onto a build plate. Nozzle follows a predetermined path building layer by layer.
https://www.3dhubs.com/knowledge-base/additive-manufacturing-technologies-overview
Uses FDM (Fused Deposition Modeling)
Most common type of 3D printing technology
Materials: Strings of thermoplastic materials
Melts materials, prints, and material solidifies as it cools.

## Slide 17: 3D Printing 101- Popular types of printing
Material Jetting: Similar to 2D printing, liquid layers are built one at a time and then exposed to light or heat to harden.
Multiple types of printing technologies under this main type
Ideal for realistic prototypes- high detail resolution and smooth surface finish
Can print in multiple colors and materials in a single print.
Negatives: High cost
https://www.3dhubs.com/knowledge-base/additive-manufacturing-technologies-overview

## Slide 18: 3D-Printing vs CNC-milling
CNC: subtractive manufacturing technology. Usually you go from a block of material to final shape.
Use 3D printing when:
  Traditional methods can’t produce the part (too complex, topology based)
  Need a fast turn-around time
  Low cost is essential and small volumes are okay
  Small number of identical parts (n<10)
  If materials cannot be easily machined (metal superalloys, or flexible TPU)
https://www.3dhubs.com/knowledge-base/3d-printing-vs-cnc-machining

## Slide 19: 3D-Printing vs CNC
https://www.3dhubs.com/knowledge-base/3d-printing-vs-cnc-machining

## Slide 20: Getting ready to 3D Print
3D-rendering
  Start with a model in CAD, Solidworks, Inventor, or other 3D rendering software
  Will need to convert it to STL
  How you convert it matters
Can find existing STL files depending on what you are trying to do.
https://www.3dhubs.com/knowledge-base/3d-printing-stl-files-step-step-guide

## Slide 21: Creating a 3D Model (Follow Inventor guidelines on BB handout)

## Slide 22: Getting ready to 3D Print: a good model
You can design great things, but if they aren’t specified for manufacturing on the desired technology, your parts will be unusable.
Fit: making interlocking pieces smaller than the surrounding piece.

## Slide 23: Getting ready to 3D print: a good model
Be careful of overhangs! We use FDM printing- anything too “sharp” of an edge will not print properly

## Slide 24: Getting ready to 3D print: a good model
Not everything needs to be 3D printed!
Things that don’t 3D print well:
  Large, flat “plate” like pieces (use other things like laser cutter)
  Really thin pieces
  Things with sharp overhangs

## Slide 25: Getting ready to 3D Print: Resolution of STL
Resolution matters:
  if too low, will have visible triangles on the surface.
  If too high, will not matter due to printing resolution so files size is increased unnecessarily.
To optimize, evaluate chord height and angle
  Chord height: 1/20th of 3D printing layer thickness, never below 1 micron.
  Angular tolerance: default 15 degrees (preset value of 0).
In general, recommend you set the “high” preset in CAD for your STL file
https://www.3dhubs.com/knowledge-base/3d-printing-stl-files-step-step-guide

## Slide 26: Getting ready to 3D Print: Wall thickness
https://www.3dhubs.com/knowledge-base/3d-printing-geometry-restrictions

## Slide 27: Getting ready to 3D Print: Part Orientation
Orientation can:
  Effect shape
  Change build time
  Change strength.
Spend time to optimize this for higher rate of success on first print.
https://www.3dhubs.com/knowledge-base/how-does-part-orientation-affect-3d-print
Notes: For two cylinders, both were printed from same file:
Horizontal took less time since 100 layers instead of 300 layers.
FDM is much stronger in XY direction than Z direction.

## Slide 28: Getting ready to 3D Print: Layer Height
Aesthetics (smoother surface) or time/cost- must decide.
Stepping effect on curves
Smaller layers have weaker mechanical properties.
Especially important for FDM
50, 200, and 300 micron layer heights
https://www.3dhubs.com/knowledge-base/impact-layer-height-3d-print

## Slide 29: Assigned Readings:
PDFs online in Blackboard Content folder:
  Fits and Design for 3D Printing
  3D Printing Reference for EASC1107
Take summarized notes and bring to class in 1 week.