## Slide 1: ECCS 2311 Electric Circuits
Signal Conditioning Design Project

## Slide 2: Project Overview
Organize into inter-department groups of 3 or 4
Design and build a signal conditioning circuit
Startup company bidding for seed funding
Pitch a proposal (in writing)
Build prototype for testing
  Use breadboard
Demonstrate working prototype

## Slide 3: Problem Description
Potentiometer position sensor used to control a joint of a robotic arm
Analog-to-Digital Converter (ADC)
  Voltage input range is [1.0V, 4.0V]
  Sinks mA of current
Fig 1 (a). Rotor diagram
Fig 1 (b). Rotor position signal

## Slide 4: System Architecture
Must design signal conditioning circuit to interface the position sensor with the ADC
Figure 2. The overall digital sensing system.

## Slide 5: Minimum Design Requirements
[1, 4] VDC signal when input is a [5, 12] VDC signal
One-to-one mapping
Affine mapping
Other criteria?
Figure 2. The overall digital sensing system.

## Slide 6: Design Hints
Op amp circuits are viable
Adjustable components are useful
  Potentiometers
    Variable resistors
  Variable Capacitors (don’t have in lab though)

## Slide 7: Project Deliverables: Team Charter
In lab on Tuesday,
  Fill out Overcoming Pitfalls of Team Projects worksheet
  Create Team Charter
    A set of rules and expectations for your team to set you up for success
Worth 5% of Project
Due Tuesday, October 3, 2017 by the end of lab

## Slide 8: Project Deliverables: Design Alternatives
At least 2 unique designs!
  Must be viable!
Mathematical Analysis
  Nodal analysis demonstrating input-output mapping
PSPICE simulations
  Demonstrating input-output mapping
  Demonstrating other criteria (e.g., power requirements)
May be handwritten with PSPICE attached
Worth 10% of Project
Due Friday, October 27, 2017
  (feedback within 1 week)

## Slide 9: Process for Creating Value Propositions: NABC Process
      Developed by SRI International
    N = Need
      What is the important customer and market Need?
    A = Approach
      What is the unique Approach for addressing this need?
    B = Benefits per Costs
      What are the specific Benefits per costs that result from this approach?
    C = Competition
      How are these benefits per costs superior to the Competition’s and the alternatives?

## Slide 10: Project Deliverables: Written Product Proposal
Required Organization
  Cover Page
  Introduction
  Problem Description
  Alternative Solution and Analysis
  Simulations
  Cost Analysis (at least 2 suppliers and 1 distributor)
  Value Proposition (NABC approach)
  Testing and Implementation
  Conclusion
  USE PRESENT TENSE in proposal (except in reflection of conclusion)!
Worth 65% of grade
Due Friday, December 1, 2017

## Slide 11: Project Deliverables: Working Prototype & Demo Pitch
5-minute pitch demonstration covering
  Problem motivation
  Functionality of circuit
  Measurement validation (showing working prototype)
  Other means to validate (simulations, test, etc.)
Worth 20%
Lab period of last week: Tuesday, December 5, 2017