## Slide 1: Intro to Arduino
Stephanie Gillespie, Ph.D.

## Slide 2: Download software
http://www.elegoo.com/download
Find Arduino IDE for your machine + training code for your kit.
When downloaded, unzip + install on your computer.

## Slide 3: What is Arduino?

## Slide 4: What is Arduino?
An open source, inexpensive embedded development platform.
Belongs to a family of programs meant to make computing accessible:
  Wiring (Embedded)
  Processing (Graphical, PC)
  Fritzing (Circuits, Hardware)

## Slide 5: What’s inside?
ATMEL AtMEGA 328
  8 bit microcontroller
  16 Mhz Operation
  6 A/D Channels (10b)
USB for Programming
Up to 19 Digital I/O channels.

## Slide 6: Arduino vs Microcontroller
Microcontroller- a compact integrated circuit designed to govern a specific operation in an embedded system. A typical microcontroller includes a processor, memory and input/output (I/O) peripherals on a single chip.
Arduino- open source platform that integrates the microcontroller with electronic components for hobbyists.
  Name brand: boards by different manufacturers will vary, software is the same.

## Slide 7: But what can we do with it?
Computer to program sensors, lights, and motors
  Pulse sensor
  Light sensor
  Muscle sensor
  Flex sensor
  Accelerometer
  Distance sensor
  Plus MORE!!!

## Slide 8: Setup
Connect board to computer via USB cable
Start Arduino.exe
  Window Key, type “arduino”, press enter

## Slide 9: Setup
Tools->Board->
Arduino Uno

## Slide 10: Setup
Tools -> Serial Port -> COM3 or higher

## Slide 11: Testing that it works!
Find the example software “blink”
Click the right arrow button to download.
Watch the messages, ensure no errors
Light should blink on/off for 1 second
Go into code, change first ‘1000’ to ‘3000’, re-download, and should see the blinking change

## Slide 12: 3 Basics of Arduino
Structure
  Layout of the code
Functions
  How to read and write data to sensors
Variables
  Data values
  HIGH/LOW, INPUT/OUTPUT, numbers, true/false

## Slide 13: Program Structure
Always 2 functions needed to write a program
  void setup() {
    Where you initialize your inputs and outputs
    Start with pinMode( pin #, OUTPUT/INPUT)
  void loop() {
    Where you write the functionality
    digitalRead – use to record the value of a sensor with a true/false option (buttons/switches)
    analogRead – use to record sensors with ranges of values
    digitalWrite/analogWrite – used to output data

## Slide 14: More functions…
To be used inside the loop() function
if ( variable == HIGH) {
  contains code for situations with specific circumstances
else {
  contains code for situations not covered in the above statement

## Slide 15: More functions…
Serial.println(variable)
  used to print values of sensors to the computer screen when plugged in
delay( # )
  will pause the program for a value in milliseconds

## Slide 16: Turn Signal Biker Jacket

## Slide 17: Secret Knock Door Lock

## Slide 18: Schematic

## Slide 19: Auto Lacing Tennis Shoes

## Slide 20: Lab Procedure
3 tasks as a group:
  Must get signoff from Peer Assistant or Faculty on each task
  Must rotate programmer on each task and record on signoff sheet.

## Slide 21: Optional Practice!
Tinkercad.com (will made an account), “circuits” section.
Write a program on the simulator
  Connect a green LED to pin 8
  Turn on a green LED for 2 seconds
  Turn off a green LED for 1 second

## Slide 22: Optional Practice
Write a program on the simulator
  Connect pin 2 to a green LED
  Connect pin 4 to a yellow LED
  Connect pin 12 to a red LED
  Turn on the green and red LED’s at the same time for 2 seconds
  Turn on the yellow LED when the green and red are off for 1 second

## Slide 23: Optional Practice
Write a program on the simulator
  Connect a push button to pin 7
  Connect a red LED to pin 12
  Turn on the LED when the button is pressed
  Turn off the LED when the button in de-pressed